## Slide 1: Build a low-powered Arm voice assistant with Google TensorFlow Lite
Karl Fezer
AI Evangelist, Arm
@karlfezer

## Slide 2: Agenda
Industry Trends
How to do machine learning on Arm Cortex-M CPUs
How to use TensorFlow Lite for Microcontrollers
Hands-on workshop!

## Slide 3: Trends

## Slide 4: The next wave of computing
1990
1993 onwards
Today
Notes: 1- Joint venture between Acorn Computers and Apple
2- Designed into first mobile phones and then smartphones
3- Now all electronic devices can use intelligent Arm technology

## Slide 5: Flexible, Scalable ML Solutions
Mali GPUs
Arm NPUs
Cortex-M/A CPUs
ML performance (ops/second)
ML capabilities
Keyword detection
Pattern training
Advanced
recognition
Smart cameras
Image enhancement
Autonomous driving
Data center
Typical ML hardware choice
Arm enables ML everywhere
Notes: Today, over 95% of AI-enabled devices are in mobile, smart home and IoT market segments and under 5% in infrastructure. (Source: IDC Cognitive Study 2018)
From this we conclude, that over 90% of the AI-enabled units being shipped today are based on Arm architecture.
The software, processors, GPUs, ML accelerators and other hardware, that we offer as part of project Trillium -> supports a huge diversity of edge use cases like the ones you can see here.
Today we will focus on the low-cost low-powered always on, always aware, devices.
Deliver use cases with multiple hardware solutions
Choose best balance of ML performance versus capabilities per use case
NPUs are highest performance
Cortex-M MCUs lowest power and cost
“Nearly all mobile inference run on CPUs” Facebook paper: Machine Learning at Facebook: Understanding Inference at the Edge Facebook Research paper January 2019 https://research.fb.com/wp-content/uploads/2018/12/Machine-Learning-at-Facebook-Understanding-Inference-at-the-Edge.pdf and https://research.fb.com/publications/machine-learning-at-facebook-understanding-inference-at-the-edge/ and
https://www.zdnet.com/article/how-facebook-deals-with-the-fact-ai-is-a-mess-on-smartphones/
Main message: ML edge requires a mass-market, scalable platform for trillions of devices
You can run ML on existing Arm CPU and GPU platforms – you don’t need a dedicated accelerator
ML Accelerators enable new use cases which weren’t possible before (anything with a tick in the fourth column)
You want a smooth transition between these devices, and so need Arm NN
All these edge devices from cars to smartphones, and even servers as Drew said yesterday, are battery constrained. Here are some examples of applications mapped to the typical ML Hardware required. However, remember there isn’t one ML workload. What ML demands is to mix and match workloads across a scalable HW platform. Pick which hardware is best to use
Most use cases today run Arm CPUs or CPUS and GPUs only. You don’t always have, or need, an accelerator. And the cloud isn’t always accessible quickly. With the choice of hardware, it’s a question of tradeoffs.
ADD TECHNICAL BENEFITS OF WHY CPUs do ML well. Most ML applications start with the CPU….Many times a CPU is all you need
ADD TECHNICAL BENEFITS OF WHY GPUs do ML well …. Many times a CPU and GPU is all you need
Some will transition to needing dedicated ML hardware. Accelerators need to support many different markets, and will come in many different forms. We need to move workloads between devices. We need to move workloads to different accelerators.
Transition: Now that I’ve given some of the important technical requirements of CPUs and GPUs and some of the use cases where they perform best with ML, what’s important for dedicated ML hardware?
Notes description:
Pattern training: i.e. like a Nest thermostat that learns when want temperature that you typically like your home set at different times
Mali has a server design win with Tencent based on HiSilicon -- NDA

## Slide 6: AI and ML Terminology
Artificial Intelligence: Umbrella term for machines acting as though they are ‘thinking’
Machine Learning: Machines adapting algorithms based on experience (e.g. labelled pictures)
Deep Learning: Machine learning using Deep Neural Network approaches
Algorithms: CNNs, RNNs, etc
Terminology
Inference
97.4% confidence
New input
Neural network w/model
A Cat
96.4% confidence
Not a Cat
Model
Training data
Neural network
Trained to recognise cats
Training
Notes: … Terminology – in business these tend to be used loosely e.g. in China ML=AI.
[CLICK]
Training:
* Big Data - lots of data available via The Internet to use for training
* Extremely important to ensure this is unbiased; valuable and needs to be protected
[CLICK]
Inference:
* To be robust, it relies on good quality training
* Assumes a correlation between the new data and the data used for training
[CLICK]
* This is not an exact science – it’s all about probabilities
- very simple classification – CAT or NOT CAT
- more complex networks can provide multiple outputs

## Slide 7: ML Edge Use Cases
Recognition and creation
Keyword spotting, speech recognition, natural language processing, speech synthesis, etc.
Any ‘signal’
Accelerometer, pressure, lidar/radar, speed, shock, vibration, pollution, density, viscosity, etc.
Images and video
Object detection, face unlock, defocus, beautification, etc.
Vision
Voice
Vibration
Notes: ML performs well at ‘patterns’ of data
Preventive maintenance

## Slide 8: Drivers for running ML on endpoint devices
Security and Privacy | Power and Cost | Reliability
Notes: Time-critical applications

## Slide 9: Machine Learning on Cortex-M CPUs

## Slide 10: TinyML
Body control unit application
Face/object detection for scene wake-up
Healthcare sensor module
Keyword spotting
Delivering on-device intelligence with “mW” of power
Intelligent anomalies detection

## Slide 11: Arm Cortex-M processor
Optimized for cost and power-efficient microcontrollers
Enhanced ML capabilities with Cortex-M4 (Arm v7E-M), Cortex-M7 (Arm v7E-M), Cortex-M33 (Arm v8-M), Cortex-M35P (Arm v8-M), supports SIMD instructions
Arm Helium technology is a new M-profile vector extension(MVE) for Arm v8.1-M architecture.
Helium will deliver 15x more ML performance and 5x signal processing
* Processor with DSP extensions
Future Cortex-M
enabled by Arm Helium technology

## Slide 12: Training a Keyword Spotting Model
Problem
Trained NN model
Deployable solution
Optimized code on HW
Need compact models: that fit within the Cortex-M system memory
Need models with less operations: to achieve real time performance
Model: Depthwise separable convolution, fully-connected, softmax

## Slide 13: Quantizing NN Solutions for Cortex-M processors
Problem
Trained NN model
Deployable solution
Optimized code on HW
Normalized Accuracy
Weight Bit-width
1.2
1
0.8
0.6
0.4
0.2
0
1
2
3
4
5
6
7
8
9
10
11
12
13
AlexNet
>7bit
VGG-16
>10bit
GoogLeNet
>9bit
SqueezeNet
>7bit
VGG-16
GoogLeNet
AlexNet
SqueezeNet
NN Model | 32-bit floating point model accuracy |  |  | 8-bit quantized model accuracy |  | 
 | Train | Val. | Test | Train | Val. | Test
DNN | 97.77% | 88.04% | 86.66% | 97.99% | 88.91% | 87.60%
Basic LSTM | 98.38% | 92.69% | 93.41% | 98.21% | 92.53% | 93.51%
GRU | 99.23% | 93.92% | 94.68% | 99.21% | 93.66% | 94.68%
CRNN | 98.34% | 93.99% | 95.00% | 98.43% | 94.08% | 95.03%

## Slide 14: Arm’s ML Computing Platform
Arm Hardware for AI/ML
Hardware Abstraction Layer
Arm Compute Library
CMSIS-Core
OpenCL
Custom API
OpenVX
Inference Engine
CMSIS-NN
ML Platform Direct Interface
Voice, Vision & Vibration Applications
Arm NN
Android NN API
CPU
Arm Cortex-A, Cortex-M, Neon, DynamIQ
GPU
Arm Mali
ML processors
Partner IPs
@graphics to update this diagram

## Slide 15: Optimizing with CMSIS-NN
CMSIS – Cortex Microcontroller Software Interface Standard
CMSIS NN provides optimized low-level NN functions for Cortex-M CPUs
  Functions implement popular NN layers: convolution, depthwise separable convolution, fully-connected, pooling, activation.
Problem
Trained NN model
Deployable solution
Optimized code on HW
Layer type | Baseline runtime | New kernel runtime | Improvement | 
 |  |  | Throughput | Energy Efficiency
Convolution | 443.4 ms | 96.4 ms | 4.6X | 4.9X
Pooling | 11.83 ms | 2.2 ms | 5.4X | 5.2X
ReLU | 1.06 ms | 0.4 ms | 2.6X | 2.6X
Total | 456.4 ms | 99.1 ms | 4.6X | 4.9X
Table: Throughput and energy efficiency improvements by layer types

## Slide 16: OpenMV

## Slide 17: TensorFlow Lite

## Slide 18: TensorFlow Lite for Microcontrollers
TensorFlow Lite Micro is designed to run on embedded systems:
  Less than 20KB binary footprint
  No memory allocation
  No library dependencies (not even POSIX or standard C/C++)
  Code is at github.com/tensorflow/tensorflow/tree/master/tensorflow/lite/experimental/micro
TensorFlow is Google’s open source machine learning framework

## Slide 19: TensorFlow Lite for Microcontrollers
Started with speech wakeword detection
Example is on GitHub
You will have it working in a few minutes!
Still a work-in-progress, but we’re improving through collaborations
https://aiyprojects.withgoogle.com/open_speech_recording
100,000 utterances, but we need more
One of the key use cases is audio

## Slide 20: SparkFun Edge Development Board
32-bit ARM Cortex-M4F processor with Direct Memory Access
48MHz CPU clock, 96MHz with TurboSPOT™
Extremely low-power usage: 6uA/MHz
1MB Flash
384KB SRAM
Dedicated Bluetooth processor with BLE 5
https://www.sparkfun.com/products/15170

## Slide 21: SparkFun Serial Basic Breakout - CH340C and USB-C
https://www.sparkfun.com/products/15096

## Slide 22: A Keyword Spotting Model
Notes: Lets start with Hardware-Constrained neural network model search : for a “Keyword spotting” use-case.

## Slide 23
Let’s get started!
codelabs.developers.google.com/codelabs/sparkfun-tensorflow/

## Slide 24: How well did it do?
Why?

## Slide 25: How well did it do?
Model accuracy decreases (slightly) due to the compression
Limitations of hardware
Noisy environment
Bias in dataset

## Slide 26: Summary
ML is moving to the IoT endpoint
Many ML use cases can be easily achieved with Arm Cortex-M CPUs
Ecosystem partnerships ensure ability to develop and deploy diverse use cases everywhere on the device
Energy grid
Smart city
Robotics
Automotive
Wearables
Sensor
Environmental
Farming
Industrial
Home automation
Identity & tracking
IoT
Healthcare
VR/AR
Smart lighting
Enterprise
Building automation
Smart watch
Retail
Connected clothing
Space
Notes: I hope we’ve established, that it is important to drive increasing intelligence from the center of the network towards the edge.
We have seen lots of technical and commercial reasons for wanting to do that.
It’s going to happen, and it is happening now.
The improvements in ML models and the way we implement them are actually making this a reality.
The work we have done has proved that it can be done and there are now lots of other teams working on it, in Arm and in the rest of the ecosystem.
The Arm offering – software, processors, GPUs, ML accelerators and other hardware, part of project Trillium -> supports a huge diversity of edge use cases like the ones we discussed today.
Today we focused on the low-cost low-powered always on, always aware, devices.
And if there is only one thing that you take away from today it should probably be this:
If you take the time to choose a model with care the benefits of doing machine learning on resource constrained edge devices, is huge!

## Slide 27: Next Steps!
Check out SparkFun – www.sparkfun.com
Check out TFLite –www.tensorflow.org/lite/microcontrollers/overview
Check out Arm Developer Pages – developer.arm.com/
Retrain the Model – developer.arm.com/armgooglevoice2019​ or
https://developer.arm.com/solutions/machine-learning-on-arm/developer-material/how-to-guides/build-arm-cortex-m-voice-assistant-with-google-tensorflow-lite/retrain-the-machine-learning-model

## Slide 29: Backup

## Slide 31: SparkFun Edge Development Board

## Slide 32: Driver issues
Mac
https://stackoverflow.com/questions/55463159/sparkfun-edge-bootloader-problems
Linux, Mac, Windows
https://learn.sparkfun.com/tutorials/how-to-install-ch340-drivers